## Slide 1: Suitable Camera and Rotation Navigation for People with Visual Impairment on Looking for Something Using Object Detection Technique
Masakazu Iwamura, Yoshihiko Inoue, Kazunori Minatani, Koichi Kise
Osaka Prefecture University
National Entrance Examination Center

## Slide 2: Difficulty for people with visual impairment
I want to drink tea, but which one is?
Person with visual impairment
People with visual impairment have a limited access to visual information

## Slide 3: Apps tell “what”
Smartphone apps can tell “what it is”
Person with visual impairment
This is tea

## Slide 4: Apps that tell visual information
Apps that can ask remote sighted people for help
Apps that use computer vision techniques
This paper focuses on this
(Not available anymore)

## Slide 5: Apps assume the object is in front
Person with visual impairment
?

## Slide 6: Apps do not tell “where”
Smartphone apps do not tell “where it is”
Person with visual impairment

## Slide 7
Unknown
Known
Task
Tools
and techniques
Current smartphone apps can be used
What
Where
Obtaining the visual
information on the object
that the user photographs
Category (i)

## Slide 8
Unknown
Known
Unknown
Known
Category (i)
Category (ii)
Task
Looking for something
Tools
and techniques
Camera with a wide field of view
(e.g., omnidirectional camera) would be useful
Current smartphone apps can be used
What
Where
Obtaining the visual
information on the object
that the user photographs

## Slide 9
Unknown
Known
Unknown
Known
Unknown
Unknown
Category (i)
Category (ii)
Category (iii)
Task
The information provided
to the user should be selected
Looking for something
Finding something valuable and unexpected to the user
Tools
and techniques
Camera with a wide field of view
(e.g., omnidirectional camera) would be useful
Current smartphone apps can be used
What
Where
Obtaining the visual
information on the object
that the user photographs

## Slide 10
Unknown
Known
Unknown
Known
Unknown
Unknown
Category (i)
Category (ii)
Category (iii)
Task
The information provided
to the user should be selected
Looking for something
Finding something valuable and unexpected to the user
Tools
and techniques
Camera with a wide field of view
(e.g., omnidirectional camera) would be useful
Current smartphone apps can be used
What
Where
Obtaining the visual
information on the object
that the user photographs
This paper focuses on this

## Slide 11: Overview of the research
In Looking for something:
  We implement a computer-vision-based prototype system that guides the user to reach the target object
  We investigate:
    whether an omnidirectional camera is more suitable than a normal camera
    We compare 5 rotation navigation methods including 3 novel voice navigation methods

## Slide 12: Agenda
Introduction
Method
User study
Conclusion

## Slide 13: Prototype system
Step 1: Object detection
Step 2: Rotation navigation
Step 3: Forward navigation
System
Backpack
Looking for my backpack
Person with visual impairment

## Slide 14: Prototype system
Step 1: Object detection
Step 2: Rotation navigation
Step 3: Forward navigation
System
Backpack
Find a backpack
at 45 deg. on the right
Looking for my backpack

## Slide 15: Prototype system
Step 1: Object detection
Step 2: Rotation navigation
Step 3: Forward navigation
System
Backpack

## Slide 16: Prototype system
Step 1: Object detection
Step 2: Rotation navigation
Step 3: Forward navigation
System
Backpack

## Slide 17: Existing Rotation Navigation
Ahmetovic+ (Percom 2019) examine 1 + 3 sound navigation methods in the context of turn-by-turn navigation
Ping
Intermittent sound (IS)
Amplitude modulation (AM)
Musical scale (MS)
Combined with Ping

## Slide 18: Ping - Existing Rotation Navigation
Ping
Intermittent sound (IS)
Amplitude modulation (AM)
Musical scale (MS)
Looking for my backpack
Ping
User with visual impairment
System
Backpack

## Slide 19: IS - Existing Rotation Navigation
Ping
Intermittent sound (IS)
Amplitude modulation (AM)
Musical scale (MS)
Interval
Far
Close
Angle
Pi
15Hz

## Slide 20: AM - Existing Rotation Navigation
Ping
Intermittent sound (IS)
Amplitude modulation (AM)
Musical scale (MS)
A 440 Hz sinusoid is modulated by a sub-audio sinusoid from 1 to 15 Hz

## Slide 21: MS - Existing Rotation Navigation
Ping
Intermittent sound (IS)
Amplitude modulation (AM)
Musical scale (MS)
Do
Re
Mi
Fa
So
La
Si
Do
The angle is subdivided into 8 circular sectors

## Slide 22: Existing Rotation Navigation
Ahmetovic+ (Percom 2019) examine 1 + 3 sound navigation methods in the context of turn-by-turn navigation
IS and MS combined with Ping were the best

## Slide 23: Proposed Rotation Navigation
3 voice navigation and 2 sound navigation methods
Left or Right (LR)
Angle (AG)
Clock Position (CP)
Intermittent Beep (IB)
Pitch (PT)
Voice navigation
Sound navigation
New

## Slide 24: Left or Right (LR) - Proposed Rotation Navigation
Left or Right (LR)
Angle (AG)
Clock Position (CP)
Intermittent Beep (IB)
Pitch (PT)
Looking for my backpack
Right, right, right, …
In front of you
User with visual impairment
System
Backpack

## Slide 25: Angle (AG) - Proposed Rotation Navigation
Left or Right (LR)
Angle (AG)
Clock Position (CP)
Intermittent Beep (IB)
Pitch (PT)
System
Backpack

## Slide 26: Angle (AG) - Proposed Rotation Navigation
Left or Right (LR)
Angle (AG)
Clock Position (CP)
Intermittent Beep (IB)
Pitch (PT)
60 degrees, right
System
Backpack

## Slide 27: Angle (AG) - Proposed Rotation Navigation
Left or Right (LR)
Angle (AG)
Clock Position (CP)
Intermittent Beep (IB)
Pitch (PT)
System
15 degrees, right
In front of you
Backpack

## Slide 28: Clock Position (CP) - Proposed Rotation Navigation
Left or Right (LR)
Angle (AG)
Clock Position (CP)
Intermittent Beep (IB)
Pitch (PT)
2 o’clock
In front of you

## Slide 29: Intermittent Beep (IB) - Proposed Rotation Navigation
Left or Right (LR)
Angle (AG)
Clock Position (CP)
Intermittent Beep (IB)
Pitch (PT)
Far
Close
Angle
Pi
Pi Pi Pi Pi … (Within 15 deg.)
Interval

## Slide 30: Pitch (PT) - Proposed Rotation Navigation
Left or Right (LR)
Angle (AG)
Clock Position (CP)
Intermittent Beep (IB)
Pitch (PT)
Far
Close
Angle
Low
High
Pitch
Low pitch
High pitch
Pi Pi Pi Pi … (Within 15 deg.)

## Slide 31: Agenda
Introduction
Method
User study
Conclusion

## Slide 32: User study: Purposes
Comparison of 5 rotation navigation methods
Selection of camera
(a) Omnidirectional camera
Omnidirectional camera
(b) Pseudo smartphone
Smartphone
Web camera
Electronic compass
Depth camera
Depth camera
Electronic compass

## Slide 33: User study: Overview
Participants: 7 people with VI
Experiments
  Comparison of 5 rotation navigation methods
  Selection of camera
Survey (interview) for looking for something was performed before the experiments
Experimenter
Participant
Target

## Slide 34: Survey on looking for something
Q4. How often do you encounter trouble in looking for something?  Mostly, more than once per week.
Q6. How do you look for something?  Mostly by groping. If available, ask a sighted person.
Q7. What item do you mostly look for?  Smartphone, earphones, cards, etc.
Q9. Where do you find lost stuff?  On a chair, table or floor. In the pocket of a jacket or bag.
For the rest, check out the paper

## Slide 35: Experiment 1: Rotation navigation
 |  | 23 F | 27 M | 27 F | 48 M | 48 M | 27 M | 34 F | Average
Voice | Left or right (LR) | 4 | 2 | 3 | 2 | 1 | 4 | 2 | 2.6
 | Angle (AG) | 4 | 4 | 3 | 5 | 3 | 4 | 5 | 4.0
 | Clock position (CP) | 5 | 2 | 5 | 3 | 4 | 5 | 3 | 3.9
Sound | Intermittent Beep (IB) | 3 | 5 | 4 | 4 | 4 | 3 | 5 | 4.0
 | Pitch (PT) | 2 | 4 | 4 | 4 | 5 | 2 | 4 | 3.6

## Slide 36: Experiment 1: Rotation navigation
No one preferred LR because it does not tell anything about the rotation angle
 |  | 23 F | 27 M | 27 F | 48 M | 48 M | 27 M | 34 F | Average
Voice | Left or right (LR) | 4 | 2 | 3 | 2 | 1 | 4 | 2 | 2.6
 | Angle (AG) | 4 | 4 | 3 | 5 | 3 | 4 | 5 | 4.0
 | Clock position (CP) | 5 | 2 | 5 | 3 | 4 | 5 | 3 | 3.9
Sound | Intermittent Beep (IB) | 3 | 5 | 4 | 4 | 4 | 3 | 5 | 4.0
 | Pitch (PT) | 2 | 4 | 4 | 4 | 5 | 2 | 4 | 3.6

## Slide 37: Experiment 1: Rotation navigation
Everybody has a different preference
 |  | 23 F | 27 M | 27 F | 48 M | 48 M | 27 M | 34 F | Average
Voice | Left or right (LR) | 4 | 2 | 3 | 2 | 1 | 4 | 2 | 2.6
 | Angle (AG) | 4 | 4 | 3 | 5 | 3 | 4 | 5 | 4.0
 | Clock position (CP) | 5 | 2 | 5 | 3 | 4 | 5 | 3 | 3.9
Sound | Intermittent Beep (IB) | 3 | 5 | 4 | 4 | 4 | 3 | 5 | 4.0
 | Pitch (PT) | 2 | 4 | 4 | 4 | 5 | 2 | 4 | 3.6

## Slide 38: Experiment 1: Reported related results
Reported related results
  Ahmetovic+ (PerCom 2019): musical experience affects the users’ behavior
  Ahmetovic+ (W4A 2019): expertise affects interaction preferences in navigation assistance

## Slide 39: Experiment 1: A comment on rotation navigation
Participant B preferred to put the target, instead of himself, at the 12 o’clock position
Proposed way
Participant B’s preference
(Target is at) 2 o’clock
(You’re at) 10 o’clock

## Slide 40: Experiment 2: Camera system
6 participants preferred omnidirectional camera
 | 23 F | 27 M | 27 F | 48 M | 48 M | 27 M | 34 F | Average
Omnidirectional camera | 4 | 4 | 4 | 5 | 5 | 3 | 5 | 4.2857
Pseudo smartphone | 3 | 2 | 5 | 3 | 3 | 1 | 2 | 2.7143

## Slide 41: Experiment 2: Pros and cons of omnidirectional camera
Pros
  I did not have to rotate to find the object
  It told me the direction of the target object
  It found the object earlier than the smartphone
Cons
  It was heavy
  Finding the bottle took time more than I expected
  The device is not common
  The “front” the system said was slightly different from my real front

## Slide 42: Experiment 2: Pros and cons of pseudo smartphone
Pros
  As I can use my smartphone, it is easy to introduce
  Easy to hold
Cons
  It was hard to capture the target object
    I needed to adjust the angle
    The system could not find the object unless it captures it, which frustrated me  I prefer to grope

## Slide 43: Agenda
Introduction
Method
User study
Conclusion

## Slide 44: Conclusion
We categorized the tasks of obtaining visual information into three
We proposed a prototype system for looking for something that used an omnidirectional camera and the use of voice in rotation navigation
A user study comprised of 7 people with visual impairment confirmed that
  (1) an omnidirectional camera is preferred
  (2) users have different preferences in rotation navigation

## Slide 45: Future work
Personalization of the system
  Finding “my” train pass
  Preferred navigation way
Existence of the object >>> Direction >> Distance
  Existence of the object is much more important than navigation
If it takes time to detect the object or fails in detection, the user thinks the object does not exist in the room

## Slide 46: Suitable Camera and Rotation Navigation for People with Visual Impairment on Looking for Something Using Object Detection Technique
Masakazu Iwamura, Yoshihiko Inoue, Kazunori Minatani, Koichi Kise
Osaka Prefecture University
National Entrance Examination Center